## Slide 1: Using Trio – Juniper Networks’ Programmable Chipset – for Emerging In-Network Applications
Mingran Yang
Alex Baban, Valery Kugel, Jeff Libby, Scott Mackie,
Swamy Sadashivaiah Renu Kananda, Chang-Hong Wu, Manya Ghobadi

## Slide 2: Data-intensive applications are the foundation of online services
Machine learning
Databases
Data analytics
Storage
Moore’s law is slowing down
We need efficient distributed systems for data-intensive applications

## Slide 3: The rise of in-network computing
Switch
Server
Server
Server
Server
Reduce latency
Improve performance
Caching: NetCache [SOSP ’17]
Database query processing: Cheetah [SIGMOD ’20]
Machine learning training: SwitchML [NSDI ’21], ATP [NSDI ’21], PANAMA [MLSys ’21]
Data Packet
Data Packet
Data Packet
Data Packet
Computation
Result Packet
Result Packet
Result Packet
Result Packet

## Slide 4: Background on data parallel distributed machine learning training
Switch
Server 1
Server 2
Server 3
Server 4
Gradients
DNN model
DNN model
DNN model
DNN model
Gradients
Gradients
Gradients
dataset
dataset
dataset
dataset
Allreduce

## Slide 5: In-network aggregation for distributed ML training
Switch
Server 1
Server 2
Server 3
Server 4
Gradients
Gradients
Gradients
Gradients
Aggregated gradients
Aggregated gradients
Aggregated gradients
Aggregated gradients
Allreduce puts significant pressure on network fabric
SwitchML [NSDI ’21] and ATP [NSDI ’21] proposed in-network aggregation
Σ

## Slide 6: Stragglers impose a practical deployment challenge with in-network aggregation
Switch
Server 1
Server 2
Server 3
Server 4
Uncorrelated performance jitter
Straggler
Must wait
There has not been much attention to straggler mitigation for in-network computing applications
Gradients
Gradients
Gradients
Gradients

## Slide 7: Enabling efficient in-network straggler mitigation in Tofino switches is challenging
Switch
Server 1
Server 2
Server 3
Server 4
Straggler
Today’s Tofino-based solutions have no in-network straggler mitigation implemented
The switch needs to perform efficient timer-based operations to mitigate stragglers
  Challenge: requires frequent interactions with the control plane

## Slide 8
Trio-ML Our proposed system for efficient in-network straggler mitigation
Achieve 1.8x faster training time for machine learning jobs by leveraging Juniper Networks’ programmable chipset.

## Slide 9
Talk outline
Overview of Juniper Networks’ chipset
Trio-ML: our proposed in-network straggler mitigation for distributed ML training
Evaluations

## Slide 10
Talk outline
Overview of Juniper Networks’ chipset
Trio-ML: our proposed in-network straggler mitigation for distributed ML training
Evaluations

## Slide 11
Tofino vs. Trio (Juniper Networks’ programmable chipset)
Tofino programmable switches
Trio-based programmable switch
Packet forwarding engine 1
Interconnection Fabric
Packet forwarding engine 3
Packet forwarding engine 2
Packet forwarding engine N
…
Parser
Deparser
Action
Match
Action
Match
Action
Match
…
Stage 1
Stage 2
Stage 3
Pipeline
Pkt
Pkt
Pkt
Thread-based architecture

## Slide 12
Packet forwarding engine 1
Packet forwarding engine 3
Packet forwarding engine 2
Packet forwarding engine N
Interconnection Fabric
…
Trio thread
Trio thread
Trio’s thread-based architecture
Trio-based programmable switch
Pkt

## Slide 13
Packet forwarding engine 1
Packet forwarding engine 3
Packet forwarding engine 2
Packet forwarding engine N
Interconnection Fabric
…
Trio’s thread-based architecture
Trio-based programmable switch
Pkt
Pkt
Pkt
Pkt
Pkt
Pkt
Pkt
Pkt
Pkt
Pkt
Trio gracefully handles non-homogeneous packet processing rates

## Slide 14
Talk outline
Overview of Juniper Networks’ chipset
Trio-ML: our proposed in-network straggler mitigation for distributed ML training
Evaluations

## Slide 15
Challenges for efficient in-network straggler mitigation
In-network straggler detection:
  Enable the switch to efficiently detect straggler events
In-network straggler recovery:
  Enable the switch to gracefully serve the job without waiting for stragglers
Requires timer-based operations based on user-defined straggler timeout
Requires a light-weight mechanism in the switch to proceed the computation
Our system, Trio-ML, addresses both challenges using Trio’s threads

## Slide 16
Challenges for efficient in-network straggler mitigation
In-network straggler detection:
  Enable the switch to efficiently detect straggler events
In-network straggler recovery:
  Enable the switch to gracefully serve the job without waiting for stragglers
Requires timer-based operations based on user-defined straggler timeout
Requires a light-weight mechanism in the switch to proceed the computation
Our system, Trio-ML, addresses both challenges using Trio’s threads

## Slide 17
Trio-ML gradient record
Server 1
Gradients
Gradients
Gradients
Gradients
Trio-ML creates a new gradient record when it receives a new packet from server
Gradient record
Record ID: 1
Job ID: Job1
List of servers: [S1, S2, S3, S4]
Received gradients: [S1, --, --, --]
Server 2
Server 3
Server 4
Trio-based switch
Trio-based switch memory
Gradient record
Record ID: 1
Job ID: Job1
List of servers: [S1, S2, S3, S4]
Received gradients: [S1, S2, --, --]
Gradient record
Record ID: 1
Job ID: Job1
List of servers: [S1, S2, S3, S4]
Received gradients: [S1, S2, S3, --]
Gradient record
Record ID: 1
Job ID: Job1
List of servers: [S1, S2, S3, S4]
Received gradients: [S1, S2, S3, S4]
Aggregated gradients
Aggregated gradients
Aggregated gradients
Aggregated gradients
Compute aggregated gradients

## Slide 18
Naïve approach for in-network straggler detection
Server 1
Straggler
Gradients
Gradients
Gradients
Gradients
Goal: detect non-responsive servers within Δ milliseconds timeout
Gradient record
Record ID: 1
Job ID: Job1
List of servers: [S1, S2, S3, S4]
Received gradients: [S1, S2, S3, --]
Server 2
Server 3
Server 4
Trio-based switch
Trio-based switch memory
Naïve approach:
The switch launches a thread and starts a timer as soon as new packets arrive

## Slide 19
The naïve approach is not scalable for large ML models
Server 1
Straggler
Gradients
Gradients
Gradients
Gradients
Server 2
Server 3
Server 4
Trio-based switch memory
Gradient record 1
(missing gradients from server 4)
Gradient record 2
(missing gradients from server 4)
Gradients
Gradients
Gradients
Gradients
Gradients
Gradients
…
Gradients
Gradients
Gradients
Trio-based switch
Servers send lots of gradient packets per training iteration
…
Gradient record 3
(missing gradients from server 4)
Trio thread
Trio thread
Trio thread
The switch would need to create one thread per packet, and is not scalable for large ML models.

## Slide 20
Trio-ML’s approach: decouple timeout threads from packet arrivals
Trio-based switch memory
Gradient record 1
(missing gradients from server 4)
…
Gradient record M+1
(missing gradients from server 4)
Gradient record (N-1)M
(missing gradients from server 4)
Gradient record 2
(missing gradients from server 4)
Gradient record M+2
(missing gradients from server 4)
Gradient record (N-1)M+1
(missing gradients from server 4)
…
…
…
…
Gradient record M
(missing gradients from server 4)
Gradient record 2M
(missing gradients from server 4)
Gradient record NM
(missing gradients from server 4)
…
…
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 0
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Thread
1
2
N
…
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Every Δ timeout interval, Trio-ML launches threads to scan gradient records

## Slide 21
Trio-ML’s approach: decouple timeout threads from packet arrivals
Trio-based switch memory
Gradient record 1
(missing gradients from server 4)
…
Gradient record M+1
(missing gradients from server 4)
Gradient record (N-1)M
(missing gradients from server 4)
Gradient record 2
(missing gradients from server 4)
Gradient record M+2
(missing gradients from server 4)
Gradient record (N-1)M+1
(missing gradients from server 4)
…
…
…
…
Gradient record M
(missing gradients from server 4)
Gradient record 2M
(missing gradients from server 4)
Gradient record NM
(missing gradients from server 4)
…
…
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Recently Referenced Flag = 1
Time out! Straggler detected
Time out! Straggler detected
Thread
1
2
N
…
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
After another Δ timeout interval, Trio-ML launches threads to scan gradient records again

## Slide 22
Trio-ML’s approach: decouple timeout threads from packet arrivals
Trio-based switch memory
Gradient record 1
(missing gradients from server 4)
…
Gradient record M+1
(missing gradients from server 4)
Gradient record (N-1)M
(missing gradients from server 4)
Gradient record 2
(missing gradients from server 4)
Gradient record M+2
(missing gradients from server 4)
Gradient record (N-1)M+1
(missing gradients from server 4)
…
…
…
…
Gradient record M
(missing gradients from server 4)
Gradient record 2M
(missing gradients from server 4)
Gradient record NM
(missing gradients from server 4)
…
…
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Time out! Straggler detected
Thread
1
2
N
…
After another Δ timeout interval, Trio-ML launches threads to scan gradient records again
Trio-ML guarantees straggler detection within [Δ, 2Δ] timeout window

## Slide 23
Challenges for efficient in-network straggler mitigation
In-network straggler detection:
  Enable the switch to efficiently detect straggler events
In-network straggler recovery:
  Enable the switch to gracefully serve the job without waiting for stragglers
Requires timer-based operations based on user-defined straggler timeout
Requires a light-weight mechanism in the switch to proceed the computation
Our system, Trio-ML, addresses both challenges using Trio’s threads

## Slide 24
Trio-ML sends partial aggregation results to recover from stragglers
Straggler
Trio-based switch
Server 1
Server 2
Server 3
Server 4
Gradients
Gradients
Gradients
Gradients
Partial aggregation result
Partial aggregation result
Partial aggregation result
Partial aggregation result
Trio-ML detects straggler
Non-straggler servers continue to make progress without waiting
Trio-ML keeps updating the straggler to ensure ML model is consistent
Partial aggregation can achieve comparable convergence performance (Yu et al., [ICML ’19])

## Slide 25
Talk outline
Overview of Juniper Networks’ chipset
Trio-ML: our proposed in-network straggler mitigation for distributed ML training
Evaluations

## Slide 26: Testbed setup
Real-world testbed
Comparisons
  Our solution: Trio-ML
  Tofino-based solution: SwitchML [NSDI ’21]
  Ideal setup: PyTorch NCCL RDMA without adding stragglers
Straggler generation pattern (Harlap et al. [SoCC ’16])
  Three possible delay points per iteration
  One server slows down at each delay point with given straggler probability p
  Delay time at each delay point: uniformly randomly chosen between 0.5x and 2x of typical iteration time
Testbed photo

## Slide 27: Impact of straggling probability on training iteration time
Chart: Straggling Probability (%)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16
SwitchML [NSDI '21] | 581.9001 | 622.8867 | 652.4546 | 730.6734 | 776.7924 | 833.6989 | 889.9914 | 966.9977 | 1055.6247
Trio-ML | 584.2239 | 587.3472 | 586.1069 | 587.3879 | 587.7224 | 592.5015 | 591.7742 | 584.0113 | 586.1929
Ideal | 590.2301 | 590.2301 | 590.2301 | 590.2301 | 590.2301 | 590.2301 | 590.2301 | 590.2301 | 590.2301
1.8 speedup
VGG11 on ImageNet dataset

## Slide 28: Trio-ML improves the time-to-accuracy by 1.60x
Chart: Time (minutes)
Trio-ML | 17.782 | 42.62 | 51.156 | 60.528 | 64.988 | 68.582 | 70.024 | 70.562 | 72.072 | 71.964 | 72.798 | 73.026 | 74.348 | 74.294 | 74.026 | 74.982 | 75.028 | 75.698 | 76.024 | 76.248 | 76.648 | 76.562 | 76.872 | 76.876 | 76.914 | 76.948 | 77.026 | 77.368 | 77.084 | 76.582 | 84.522 | 84.968 | 84.554 | 84.968
VGG11 on ImageNet dataset
80% Target Accuracy
1.60× speedup
Similar gains for ResNet50 and DenseNet161

## Slide 29
Conclusion
Stragglers impose a deployment challenge for in-network computing solutions.
Trio-ML: a novel in-network straggler mitigation system using Juniper Networks’ thread-based programmable chipset.
Trio-ML outperforms today’s in-network aggregation solutions by up to 1.8x.
Please email mingrany@mit.edu for more information!